Stormwater Construction Site Inspection Report

Note:

- The General Information section (page 1) of this report is to be filled out for all construction site inspection activities.

- All pages of this inspection report along with Site Disturbance Permit, Notice of Construction, EPSC Plans, and Notice of Intent (if applicable) must remain on site during construction activities and made available to the MSD inspector upon request.

- Page 2 of this report is to be used for each inspection. Each BMP shown on the Erosion Prevention & Sediment Control Plan must be inspected and noted by the EPSC Certified Inspector every 7 calendar days & within 24 hours of a half inch or greater storm event.

- All repairs and maintenance should be completed within 48 hours from the date of inspection.

- Any BMP deletions from the approved plan must be redlined and approved by MSD Development Team.

- Adding to or extending an approved BMP must be marked on plan and shown to MSD Inspector.

- This form & MSD Rain gauge information may be downloaded from MSD’s website at www.msdlouky.org

- Refer to the “Site Inspection Guidelines” form located on MSD’s website at www.msdlouky.org  for guidance on inspecting specific BMP’s.

- Number the structural and non-structural BMP’s identified in your Storm Water Pollution Prevention Plan (EPSC Plan), and list them below. Carry a copy of this report and plans with you during your inspections to ensure that you are inspecting all required BMP’s on your site

General Information

Project Name _________________________________________________________________

Project Start Date __________________                 Site Disturbance Permit No. _____________

Date of Preconstruction Meeting?   ______________

Note: A Pre construction meeting is highly recommended to ensure all parties involved in the construction phasing, installation, and/or maintenance of Erosion Prevention & Sediment Control BMP’s, etc., can be followed in the manner described on the approved plans.

Who attended? (Check all that apply)        Owner   Contractor   MSD Inspector   MSD Plan Reviewer

Were changes made to EPSC Plan? Yes   No

Stormwater Construction Site Inspection Report

Project Name: _______________________________                                                                  Date of Inspection: ____________

Type of Inspection:   Weekly     Post-storm event   (greater than 0.5 inches in 24hr. period)

Date of storm event _____________            Amount of Rain ________ Inches       Stage of Construction (% complete) __________%

| BMP # & Description (List all BMP’s on plan or added in field) | BMP Installed & Operating properly? | Corrective Action Needed? (If No is checked, specify action needed in space provided) | Date of corrective action/responsible person |
| --- | --- | --- | --- |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |
|  | (Yes (No |  |  |

Comments:______________________________________________________________________________________________________________________________________________________________________________________________

________________________________________________________________________________________________________________________________________________________________________________________________________

Page: _____of____

Overall Site Issues

Below are some general site issues that should be assessed during inspections.  Customize this list as needed for conditions at your site.

|  | BMP/activity | Implemented? | Maintenance Required? | Corrective Action Needed and Notes |
| --- | --- | --- | --- | --- |
| 1 | Are all slopes and disturbed areas not actively being worked properly stabilized after 14 days? | (Yes (No | (Yes (No |  |
| 2 | Are natural resource areas (e.g., streams, wetlands, mature trees, etc.) protected with barriers or similar BMPs? | (Yes (No | (Yes (No |  |
| 3 | Are perimeter controls and sediment barriers adequately installed (keyed into substrate) and maintained? | (Yes (No | (Yes (No |  |
| 4 | Are discharge points and receiving waters free of any sediment deposits? | (Yes (No | (Yes (No |  |
| 5 | Are storm drain inlets properly protected? | (Yes (No | (Yes (No |  |
| 6 | Is the construction exit preventing sediment from being tracked into the street? | (Yes (No | (Yes (No |  |
| 7 | Is trash/litter from work areas collected and placed in covered dumpsters? | (Yes (No | (Yes (No |  |
| 8 | Are washout facilities (e.g., paint, stucco, concrete) available, clearly marked, and maintained? | (Yes (No | (Yes (No |  |
| 9 | Are vehicle and equipment fueling, cleaning, and maintenance areas free of spills, leaks, or any other deleterious material? | (Yes (No | (Yes (No |  |
| 10 | Are materials that are potential stormwater contaminants stored inside or under cover? | (Yes (No | (Yes (No |  |
| 11 | Are non-stormwater discharges (e.g., wash water, dewatering) properly controlled? | (Yes (No | (Yes (No |  |

Certification Statement

“I hereby certify under penalty of law that by signing as the On Site Contractor Representative, the installation & maintenance of all erosion & sediment control BMP’s, and the completion of the Stormwater Construction Site Inspection Report will be performed by me or by an EPSC certified person under my direction and supervision and the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.  I am aware that there are penalties and fines for submitting false information, including the possibility of revoking my EPSC Certification.”

Signature: _________________________________________________________  Date:_____________________

EPSC Certification #:  __________________      Expiration Date:  _________________   Mobile #: ____________________________